## Slide 1
IIT BOMBAY — DEPARTMENT OF MECHANICAL ENGINEERING
Simulation Based
Toolpath Generation
& Validation for
Robotic Milling
An End-to-End Workflow from CAD/CAM to Physical Robot Execution
Presenters: Aayush Shah, Shashwat Agrawal, Ishaan Mondal, Kartik Goyal
Institution: IIT Bombay
Date: 18/04/2026

## Slide 2
Section 1 — Introduction & Objectives
Robotic Milling & The Post-Processor Gap
What is Robotic Milling?
Robotic milling uses 6-DOF articulated industrial arms for subtractive machining — milling, drilling, trimming, contouring — replacing conventional CNC tools.
Key Advantages over CNC
Larger reachable workspace
Full orientation dexterity
Access to complex undercuts
Freeform geometry capability
The Fundamental Technical Gap — Post-Processors
CNC Milling (Mature Ecosystem)
G-code is universal fairly universal, post-processors are mature, validated, commercially available for virtually every CAM–machine pairing.
Robotic Milling (Fragmented Ecosystem)
No universal standard — Mitsubishi, FANUC, KUKA, ABB, Yaskawa each use proprietary motion languages and coordinate conventions.
The Post-Processor Gap
CNC Milling Pipeline
CAD
CAM
Post-Processor
G-code
CNC Controller
Robotic Milling Pipeline
CAD
CAM
Post-Processor
Joint + TCP
Robot Controller
RoboDK: The Bridging Platform
Accepts toolpaths from Fusion 360
Full kinematic simulation & verification
Generates controller-specific programs
The intervention point enabling this workflow

## Slide 3
Section 1 — Introduction & Objectives
Research Objectives
2
TCP Calibration
Characterize and resolve TCP-to-flange calibration for spindle-mounted milling tool, including handle geometry challenges and pose variability
4
Failure Identification
Identify, document, and resolve systematic failure modes in code export, file parsing, and controller upload pipeline
5
API-Based Analysis
Lay computational groundwork for jerk and stiffness analysis using RoboDK Python API for dynamic performance optimization
1
Toolpath Exploration and Selection
Investigate and compare different toolpath strategies in Fusion 360, analyzing their suitability for various geometries and identifying optimal toolpaths for accurate and efficient machining.
3
Workflow Validation
Establish validated end-to-end simulation-based workflow from Fusion 360 CAD/CAM to physically executable motion programs on a Mitsubishi robot

## Slide 4
Section 2 — Methodology
End-to-End Workflow Architecture
Complete Pipeline — Four Major Stages
Fusion 360
CAD + CAM
Part geometry, stock, toolpath, post-processor export
Multi Stage Validation
RoboDK
The architectural spine: Two layer verification eliminating risk of discovering errors only at physical execution.
Simulation + Validation
Layer 1 — RoboDK (Kinematic Level)
TCP setup, kinematic simulation, reachability checks
Reachability validation
Singularity detection
Joint limit compliance
Frame consistency
Layer 2 — RT Toolbox 3 (Controller Level)
RT Toolbox 3
Syntax compatibility
Controller-Native Sim
Motion command validation
Parser validation, syntax verification, program execution
Program structure verification
Controller-native parser
Why Validation is Necessary
Robot post-processors are fragmented and unreliable, making CAD/CAM outputs inherently untrustworthy.
Strict Validation Principle
Physical Robot
Dual simulation embeds validation directly into the workflow through independent kinematic and controller-level checks, ensuring errors are detected before physical execution.
Execution
1
Program upload, physical cutting, quality verification
Fusion 360 → Toolpath correctness
2
RoboDK → Kinematic feasibility
3
RT Toolbox 3 → Controller compatibility
4
Physical Robot → Execution validation

## Slide 5
Section 2 — Methodology
From CAD to Simulation — Fusion 360 to RoboDK
Part A — CAM Toolpath Generation in Fusion 360
1. Part Geometry & Stock Definition
Part designed or imported; stock geometry explicitly defined for material removal computation and collision detection.
2. Machining Operations
Operations constructed in Manufacture workspace:
Facing
3D Contouring
Parallel Passes
Pocket Milling
Multi-Axis Simultaneous
3. Tool Library Entry
Tool library entry matches physical tool geometry, used for selecting the most appropriate tool for the process.
4. RoboDK Integration via Plugin
CAM toolpaths are programmatically imported into RoboDK for simulation, enabling a seamless transition from Fusion 360 to the robot environment.
Part B — RoboDK Simulation Environment Setup
Robot Model Import
Physical robot model (Mitsubishi RV series) imported from built-in library — accurate kinematic model.
Three Main Coordinate Frames Defined
W
World / Base Frame
Root at robot base — all spatial references expressed relative to this
Wp
Workpiece Frame
Part coordinate system positioned relative to base
TCP
Tool Frame (TCP)
Functional tool tip relative to flange - most technically demanding
Toolpath Import & Validation
Fusion 360 toolpath imported with correct frame assignment; reachability and singularity checks run across all targets.
Validation Checks
All targets within joint limits
No singular configurations
Consistent wrist configuration

## Slide 7
Section 2 — Methodology
TCP Calibration & Reference Frame Finalization
The TCP — Definition and Stakes
Tool Center Point (TCP): precisely defined reference point at functional cutting tip, expressed as position/orientation offset relative to robot flange.
Critical Consequence of TCP Error
Calibration error of even 1mm in any TCP offset component produces same 1mm positional error at every single toolpath target — global systematic offset.
Why Spindle-Mounted TCP took us time.
Milling Spindle (Complex)
Mounted via custom bracket and handle assembly:
Large offset through multiple interfaces
Spindle can shift/tilt depending on tightening
Pose variability between measurement sessions
Single measurement insufficient

## Slide 8
Section 3 — Experimental & Modeling Work Done
Experimental Setup & Initial Validation Testing
Physical Laboratory Setup
Robot Hardware
Mitsubishi RV series 6 DOF robot with milling spindle mounted via custom bracket/handle assembly.
Workpiece Fixture
Positioned on rigid table within reachable workspace — maximizing reachability while maintaining safe clearance.
TCP-IP Communication
Bidirectional link between RoboDK (PC) and Mitsubishi controller for real-time joint streaming and command transmission.
Experiment 1 — Live Joint Coordinate Verification
Procedure
Current joint angular positions (all six joints) streamed live from controller into RoboDK.
Observation
Simulation model mirrored physical robot pose instantaneously — confirming kinematic model correctness.
Significance
Essential sanity check: if simulation and physical robot disagree about configuration, all subsequent simulation results are meaningless.
Result
Live joint readout confirmed model physical synchronization — prerequisite condition satisfied.
Experiment 2 — Manual Target Dry-Run
Procedure
Simple manual targets programmed in RoboDK, uploaded to controller, executed in free air (no workpiece contact).
Purpose
Validate basic motion program upload pipeline before introducing complex multi target toolpath.
Result
Robot moved to all manual targets accurately — basic communication, file transfer, and execution pipeline functional.
Critical Insight
This success set an expectation that complex toolpaths upload would be straightforward.

## Slide 9
Section 3 — Experimental & Modeling Work Done
Learning Curve: Code Upload Failure & The RT Toolbox 3 Pivot
The Attempt — Complex Toolpath Upload
Full multi-target complex toolpath exported from RoboDK in Mitsubishi .PRG format and uploaded to controller using RoboDK itself.
Result
Controller rejected program outright with parse error — no motion executed, only generic fault code produced. (Unexpected movement of the robot)
Diagnosis Attempts — What Was Tried
1. Manual .PRG File Examination
Reviewed header structure, motion commands (MOVL, MOVJ, MOVC), label formatting, speed parameters, frame declarations.
2. Controller Pendant Diagnostics
Accessed error logs — returned generic fault codes with insufficient information to pinpoint specific cause.
3. Systematic Candidate Iteration
Tested motion type, speed format, frame conflicts, program name restrictions, header formatting — root cause not identified.
The Strategic Pivot — RT Toolbox 3
After exhausting direct upload debugging, we tried using Mitsubishi's official offline programming environment.
What RT Toolbox 3 Provides
Full kinematic simulation (same engine as controller)
Detailed line-referenced error logging
Same parser as physical controller
Complete virtual program validation
Execution
.PRG imported and simulated virtually — issues surfaced with actionable specific error messages that pendant failed to provide. (However the direct upload over RoboDK still doesnt work)
Result
Program iteratively corrected until clean simulation — structurally necessary intermediate validation gate.
Updated Pipeline Architecture
RoboDK
RT Toolbox 3
Controller

## Slide 10
Section 3 — Experimental & Modeling Work Done
Finalized End-to-End Workflow
Primary methodological contribution: Definitive validated workflow — every step grounded in lessons from preceding experimental iterations.
1
Fusion 360
Part geometry, stock, strategy, toolpath, tool library, post-processor export
2
RoboDK Setup
Robot import, world/workpiece/tool frame definition, toolpath import
3
Live Sync
Joint positions via TCP-IP, simulation synchronized to real-world
4
TCP Application
Calibrated values as Tool Frame, transformation chain verified
5
Workpiece Reg.
Robot jogged to touch workpiece at reference point, pose recorded
6
Toolpath Alignment
TCP aligned with targets, joint angles extracted, reachability verified
7
RoboDK Validation
Complete toolpath simulated, kinematic errors identified and corrected
8
.PRG Export
Motion program exported in Mitsubishi .PRG format
9
RT Toolbox 3
Native simulation, no syntax/motion errors confirmed
10
Physical Exec.
Dual-validated .PRG uploaded and executed on physical robot
Validation Status
Kinematically verified
Controller-validated
Physically executed

## Slide 11
Section 4 — Key Findings
Key Findings
1
Dual-Simulation Validation is Structural Necessity
Direct RoboDK to controller pipeline unreliable without controller-native intermediate simulation.
Non-Redundant Error Detection
RoboDK Catches:
• Reachability failures
• Singularities
• Joint limit violations
• Frame misassignments
RT Toolbox 3 Catches:
• Syntax incompatibilities
• Command mismatches
• Structure failures
• Parser errors
2
TCP Calibration is a High Risk Single Step
TCP error is uniquely dangerous — globally propagating, single error affects every target identically, impossible to detect from machining error pattern alone.
Spindle Handle Variability
Spindle handle-induced pose variability is practically significant, systematically underestimated source of TCP uncertainty — must be managed through repeated measurement.
Future Recommendation
Formal TCP auto-calibration routine — robot touches fixed precision reference sphere from multiple orientations, controller solves TCP analytically.
3
Multi-Axis Toolpath Simulation Successfully Validated
Multi-axis milling toolpaths for complex freeform geometries successfully generated in Fusion 360 and validated in RoboDK — smooth, continuous, singularity-free motion.
Validation Evidence
Correct TCP orientation maintained throughout
Robot arm continuously reorienting for tool-surface normal alignment
No kinematic violations detected
Capability Confirmed
RoboDK is production capable for multi-axis robotic milling program generation; workflow generalizable to new geometries.

## Slide 12
Section 4 — Key Findings
Key Findings

## Slide 13
Section 5 — Remaining Work
Remaining Work I — Literature Landscape & Research Gaps
Topic Cluster 1 — Robotic Milling Accuracy
Systematic Comparison
Positional and orientational accuracy: robotic milling vs. conventional CNC machining.
Error Source Characterization
Documented sources of dimensional error:
• Joint compliance and backlash
• Thermal drift
• TCP calibration error
• Base-frame registration error
Topic Cluster 2 — TCP Calibration Methods
Methodology Survey
• Manual gauging (used in this work)
• 4-point and multi-point touch-off routines
• Vision guided calibration approaches
Quantitative Comparison
Achievable TCP calibration accuracy across methods — assessing whether manual approach is within acceptable band.
Spindle-Mounted Tool Focus
Specific focus on spindle-mounted tools where handle geometry and mount variability create documented challenges.
Topic Cluster 3 — Simulation-Based Validation
Framework Review
Existing tools and how they handle RoboDK to controller gap:
Dual-Simulation Survey
Are there published workflows using dual-simulation (CAM-side + controller-native) similar to RoboDK + RT Toolbox 3?
Post-Processor Evaluation
How do researchers validate robotic post-processor correctness without exhaustive physical testing?